## Slide 1: A.O. Smith Options With Microchip and Microsoft Azure IoT
October 2021
JR & RW

## Slide 2: Current Solution
uRata
Application MCU – (NXP Kinetis)
BLE
(unused)
BCM43
STM32
Security?
Networking: TCP/IP, TLS
Ayla Production Agent
A.O. Smith Application
(No RTOS)

## Slide 3: Azure IoT Central With SAM-IoT
https://github.com/Azure-Samples/Microchip-SAM-IoT-Wx/blob/main/SAM_IoT_Central.md

## Slide 4: Option 1: Partitioned Embedded Cloud Agent
Application MCU SAMD54
WiFi/BLE WINC3400*
Cloud Agent MCU
SAMD21
ECC608
Benefits
Partitioned, straightforward firmware similar to existing architecture
Secure element
Separate MCU- easier switchover to Azure-IoT
Eliminates discrete BLE
Concerns
Double MCU implementation
“Agent” development
Simple Prototype
(WINC1510 +
SAMD21 +
ECC608B)
*Or WINC1510 (WiFi Only)
A.O. Smith Application
(No RTOS)
Azure-IoT “Agent” replace
Ayla Portable Agent
Hardware Secure Element
Networking: TCP/IP, TLS 1.2, WiFi, BLE

## Slide 5: Option 2: App MCU + WFI32 for all Networking
MCU+WiFi
WFI32
ECC608
Concerns
No BLE
Benefits
Little change to application FW
Simplify design- 2 chip solution
Built-in secure element
Application MCU SAMD54
Azure-IoT “Agent” together with
Networking: TCP/IP, TLS 1.2, WiFi, WPA3
(Azure RTOS)
Secure Element
RN-Azure
A.O. Smith Application
(No RTOS)

## Slide 6: Option 3: Merged Cloud Agent with Application
Application MCU SAMD54 w/Azure RTOS
WiFi/BLE WINC3400*
ECC608
Benefits
Condensed firmware
Single MCU
Existing application running under an RTOS
Eliminates discrete BLE
Concerns
1 MB Flash
Heavier software effort to merge existing control with connectivity functions
*Or WINC1510 (WiFi Only)
Networking: TCP/IP, TLS 1.2, WiFi, BLE
A.O. Smith Application + Azure-IoT “Agent” running together under Azure RTOS
Hardware Secure Element

## Slide 7: Option 4: Merge Everything into a Single Device
All in 1 MCU+WiFi
WFI32
ECC608
Concerns
1 MB Flash
Heaviest software effort to merge all functions
No BLE
Benefits
Condensed firmware
Single device- board space, layout
Built in secure element
A.O. Smith Application,
Azure-IoT Agent together with
Networking: TCP/IP, TLS 1.2, WiFi, WPA3
(Azure RTOS)
Secure Element

## Slide 8: Recommended for Eval: SAM-IoT Dev Board
Easy Azure Connectivity for 32-bit ARM based Embedded Applications
  Embedded sensors, actuators or mechatronic applications
  Easy to add cloud connection to huge install base of SAM MCU applications
Smart: SAMD21 MCU
  Low power down current
  Great combination of large memory, ultra low power and rich feature set
Connected: WINC1510 Wi-Fi
  Running TCP/IP and TLS connection to Azure
Secure: ATECC608A
  Key storage, Authentication, Crypto
  Secure device authentication to Azure
  Secure provisioning support
https://www.microchip.com/en-us/development-tool/EV75S95A
Voltage Regulator
(MIC33050)
mikroBUS
Connected
ATWINC1510
nEDBG
Drag’n Drop
Serial/USB
Prog/Debug
Battery Charger
MCP73871
Secure
ATECC608A
Smart
SAMD21
2 in / 5 cm
1 in / 2.5 cm
Temp Sensor
(MCP9808)
Light Sensor
(TEMT6000)
Indicator LEDs
Micro USB
Connector
Notes: 1 min

## Slide 9: Proof of Concept Demo using SAM-IoT Board
Application MCU
2KB
Bucket #4
Bucket #3
Bucket #2
Bucket #1
2KB
2KB
2KB
GOALS
Confirm IoT Hub receives data using Azure IoT Explorer
All 4 operations should be completed within 5 seconds
Azure IoT Hub

## Slide 10: Azure IoT PnP Interface for SAM-IoT (version 2)
Azure Cloud
Telemetry
Brightness
Temperature
Button events
Properties
Blue LED state
Green LED state
Yellow LED state
Red LED state
Telemetry interval
Commands
Reboot
Azure Device Model
(“SAM_IoT_WM;1”)
SAM-IoT Board
Sensors
- Light
- Temperature
4 LEDs
2 Buttons
Integers (4)
Strings (4)
Boolean (1)
Doubles (2)
Floats (2)
Long (1)
ADD
Integers – read only by cloud (2)
Integers – writable by cloud (2)
IP Address (read only string)
WINC1510 FW Version (read only string)
ADD
Send ASCII Message
ADD
2
MQTT

## Slide 11: Application Parameters – Direction of Data Flow
Azure Cloud
Telemetry
Brightness
Temperature
Button events
Properties
Blue LED state
Green LED state
Yellow LED state
Red LED state
Telemetry interval
Commands
Reboot
Azure Device Model
(“SAM_IoT_WM;2”)
SAM-IoT Board
Sensors
- Light
- Temperature
4 LEDs
2 Buttons
Integers – read only by cloud (2)
Integers – writable by cloud (2)
Integers (4)
Strings (4)
Boolean (1)
Doubles (2)
Floats (2)
Long (1)
Send ASCII Message
MQTT
Strings (IP Addr & FW ver) – read only

## Slide 12: Command Line Interface (CLI) for SAM-IoT
MQTT
Azure Cloud
Application MCU
UART (460,800 baud)
Telemetry Reported to Cloud
Properties Sync’d with Cloud
Update Telemetry & Properties using ASCII commands via Command Line Interface (CLI)
CDC Interface (1200 to 500K baud)

## Slide 13: Standard ASCII Commands for SAM-IoT CLI
Help
Command Format | Action
idscope [ID Scope] | Get and set Azure DPS ID Scope
reconnect | MQTT reconnect
wifi <ssid>[,<pass>,[authType]] | Set Wi-Fi credentials (authType: 1 = Open, 2 = WPA, 3 = WEP)
wifi –[scan¦status] | Get list of Wi-Fi SSID’s or connection status
key | Get ECC public key
device | Get ECC serial number
cli_version | Get CLI version
version | Get firmware version
debug [level] | Get and set debug level
reset | Reset host
q | Quit command processor
help | Help menu
ADD
Notes: Connection status – error in communication?

## Slide 14: Application Command using CLI [telemetry]
index | description | name | schema | CLI Example | Action / Result
1 | App Telemetry signed integer #1 | telemetry_Int_1 | integer | >telemetry 1,FE | telemetry_Int_1 = 254
2 | App Telemetry signed integer #2 | telemetry_Int_2 | integer | >telemetry 2,BA6E | telemetry_Int_2 = 47,726
3 | App Telemetry signed integer #3 | telemetry_Int_3 | integer | >telemetry 3,609D64 | telemetry_Int_3 = 6,331,748
4 | App Telemetry signed integer #4 | telemetry_Int_4 | integer | >telemetry 4,C36941E5 | telemetry_Int_4 = -1,016,512,027
5 | App Telemetry double #1 | telemetry_Dbl_1 | double | >telemetry 5,F537A021CF015B44 | telemetry_Dbl_1 = -4.43422395117885722194330763894E256
6 | App Telemetry double #2 | telemetry_Dbl_2 | double | >telemetry 6,9D1F2C043A774B55 | telemetry_Dbl_2 = 1.0367692620813990098267580227E-305
7 | App Telemetry float #1 | telemetry_Flt_1 | float | >telemetry 7,418345E1 | telemetry_Flt_1 = 16.40912
8 | App Telemetry float #2 | telemetry_Flt_2 | float | >telemetry 8,C20508DE | telemetry_Flt_2 = -33.25866
9 | App Telemetry Long | telemetry_Lng | long | >telemetry 9,CAFE1234BEEF5678 | telemetry_Lng = 14,627,148,657,496,905,336
10 | App Telemetry Boolean | telemetry_Bool | boolean | >telemetry 10,true | telemetry_Bool = true
11 | App Telemetry String #1 | telemetry_Str_1 | string | >telemetry 11,hello | telemetry_Str_1 = hello\0
12 | App Telemetry String #2 | telemetry_Str_2 | string | >telemetry 12,goodbye | telemetry_Str_2 = goodbye\0
13 | App Telemetry String #3 | telemetry_Str_3 | string | >telemetry 13,Hi!!! | telemetry_Str_3 = Hi!!!\0
14 | App Telemetry String #4 | telemetry_Str_4 | string | >telemetry 14,Bye!!! | telemetry_Str_4 = Bye!!!\0
Command: “telemetry”
Application MCU transmits its own telemetry updates using one of the storage slots in the table by choosing the desired index
> telemetry <index>,<data>

## Slide 15: Enhancement: Dedicated Telemetry Interface (UART)
Application MCU
UART 921.6Kbaud
INT (PA24)
TXD (PA08)
RXD (PA09)
MQTT
Index Byte | Length (MSB) | Length (LSB) | Data Byte | . . . . . . . . . . . | Data Byte
TXD
/INT
SERCOM2
Azure Cloud
Send Telemetry Data Frame after generating interrupt
Larger telemetry strings can get updated faster
Minimum Rx buffer size = (3 + 1024) bytes = 1027 bytes
Notes: 4096 Bytes = 2048 Words = 1024 Integers
1. (5000 milliseconds / 2048 Words) = 2.44 msec per update
2. (5000 milliseconds / 1024 Integers) = 4.88 msec per update

## Slide 16: Enhancement: Dedicated Telemetry Interface (SPI)
Application MCU
(SPI Master)
CS (PA06)
SCK (PA05)
MOSI (PA04)
MISO (PA07)
MQTT
Index Byte | Length (MSB) | Length (LSB) | Data Byte | . . . . . . . . . . . | Data Byte
MOSI
/CS
SERCOM0
Azure Cloud
Send Telemetry Data Frame after setting Chip Select
SAMD21G18A
(SPI Slave)
48 MHz
Larger telemetry strings can get updated faster
Minimum Rx buffer size = (3 + 1024) bytes = 1027 bytes
Notes: 1. (5000 milliseconds / 2048 Words) = 2.44 msec per update
2. (5000 milliseconds / 1024 Integers) = 4.88 msec per update

## Slide 17: Application Command using CLI [property]
index | description | name | schema | writable (by Cloud)
1 | App Property #1 | property_1 | integer | false
2 | App Property #2 | property_2 | integer | false
3 | App Property #3 | property_3 | integer | true
4 | App Property #4 | property_4 | integer | true
> property <index>,<data(hex)>
CLI Examples
Update Property #1 with a bitmask of 01110100b
> property 1,76
Update Property #3 with a value of 20,000
> property 3,4E20
Confirm that new value of Property #4 has been changed to 51,996 (after receiving the change request from the SAM-IoT)
> property 4,CAFE
Command: “property”
Application MCU communicates information about itself (e.g. state or configuration) using any of the properties (which can be read by the cloud on demand whenever needed). If the property is defined as writable by the cloud, this means the cloud is also allowed to change the value. In this case, the property command is also used as a confirmation response message (i.e. serving as an ACK to the SAM-IoT which will then send an ACK to the cloud).

## Slide 18: Property Write from the Cloud (writable = true)
Azure Cloud
Application MCU
1. Send New Property Value
4. Send ACK to complete sync
Writable properties can be changed from the Cloud
SAM will notify APP of the updated property by sending an ASCII message on the CLI PROP<x>=<new_value(hex)> (e.g. “PROP3=BEEF”)
Application must confirm the change using the property command as the ACK response
2. Send New Property Value
PROP<x>=<new_val(hex)>
3. Send Confirmation (ACK)
property <x>,<new_val(hex)>
UART
MQTT

## Slide 19: Read-only Properties (writable = false)
Azure Cloud
Application MCU
Cloud cannot change read-only properties
Typically used for Application to sync its state information with the cloud
1. Update Property #<x>
property <x>,<new_val>
UART
MQTT
2. New property value is synchronized with the cloud

## Slide 20: Command: Send ASCII Message (from the Cloud)
Azure Cloud
Application MCU
Send ASCII message
(1024 chars max)
Quick way to send an arbitrary ASCII string from the Cloud to the Application MCU
2. ASCII message echoed on the console
UART
MQTT

## Slide 21: Azure Code Examples Provided by Microsoft
Developers get full MPLAB X projects from Microsoft-owned GitHub repositories
PIC-IoT https://github.com/Azure-Samples/Microchip-PIC-IoT-Wx
SAM-IoT https://github.com/Azure-Samples/Microchip-SAM-IoT-Wx
SAME54-XPRO https://github.com/azure-rtos/samples
PIC32 WFI32E Curiosity TBD (UNDER CONSTRUCTION)
ATSAMA5D27 Wireless SOM TBD (UNDER CONSTRUCTION)
START HERE
Notes: 4 blocks of 1KB every 5 seconds